## Slide 1: SV8100 – Management
Pre-Sales Support
UNIVERGE SV8100
Release 9
Doc. Version 9.01

## Slide 2: Overview
PCPRO
  Offline Programming with PC application
  Graphical User Interface
  Offline
WebPro (UserPro)
  Programming via Web interface
  Graphical User Interface
  Changes are immediately effective
End UserPro
Phone Programming
  Programming via System Phone
  Coded commands
  Changes are immediately effective

## Slide 3: PCPro
Offline Programming with PC application
Graphical Interface
  Data can offline be prepared and Uploaded later to the SV8100
  Data can be downloads
  Easy to make Backup
Programming
  Wizzard at 3 levels
    Mandatory
    Optional
    Advanced
  System data Programming
    Only to be used by experienced engineers
Help Information
  Contains features and Specification Manual

## Slide 4: Graphical Interface
Submenu
Main menu
Toolbar
Work space
Status bar
PCPro
Wizzards

## Slide 5: System data Programming
PCPro
Program Codes

## Slide 6: Connection
Connecions
  LAN For security reasons the local CPU-IP port can be used i.s.o. the VoIP port
  Remote ISDN-BRI connect to a build-in ISDN Modem (DDI to 308)
Password protected User Accounts
  4 User levels
    Tech Installer Mode (IN)
    System Administrator Mode 1 (SA)
    System Administrator Mode 2 (SB)
    User Administrator (UA)
  1 session active at a time
Each User Accounts can define a range of Connection accounts
PCPro

## Slide 7: WebPro
WebPro
  Connect via Web browser tot the SV8100
    Maintenance interface integrated in the SV8100
    No special software needed of pc of System Administrator
  Changes are Immediately effective
  Save and restore System of System database
    Save in Compressed file (.gz)
    file can not be viewed within Webpro
    After Uncompress it can be viewed in PCPro
  Upgrade SV8100 Main Software
    PZ-ME50 card required
    NO USB memory required

## Slide 8: WebPro
Connecion
  LAN For security reasons the local CPU-IP port can be used iso the VoIP port
  Remote ISDN-BRI connect to a build-in ISDN Modem (DDI to 308)
  Password protected 2 access levels
    System Administrator (UA Level)
      System wide changes
    User (UB Level) (UserPro)
      Only allowed to make changes for that extension that that logs in (Ext. nr. is login name)
      Can be translated in local language
  4 sessions active at a time

## Slide 9
WebPro

## Slide 10: Phone programming
Program the SV8100 via a system Phone
  Use codes as used in PCPro System data programming eg 15-22-01 (Mobile extension setup)
Enter Command Mode by prseeing SPK #*#* “Password” Transfer
Use Keys to navigate through programming
  Transfer = Store/Next
  Hold = Clear
  Answer = Back
  MIC = Scroll
  SPK = Exit
  Navigation button
    Up = Next port
    Down = Previous port
    Left/Right = Name edit

## Slide 11: PCPro Practical
Confirm IP Address of system
  10-12-01 Ethernet connection
  10-12-09 IPLA Connection
Notes: 10-12 -01 CCPU, 10-12-09 IPLA

## Slide 12: End User Pro
One of the installable add-ons from the Desktop Suite
Shows phone details and allows programming of own function keys

## Slide 13: IP Phone Manager
Way of working:
Specify subnet
Search IP phones which comply with the search algorhytm
Upgrade firmware to these phones
Telephone management:
IPPhone Manager – upgrade DT700 phones with new firmware
PCPro – change settings (e.g. button progr.) on individual phones

## Slide 15: Document History
17-03-2011 .
  Copyright statement changed
29-05-2013 Doc. Version 9.00
  Webpro enhancements (save configuration, Upgrade firmware)
  User Pro can easily be translated in Local Language
04-06-2013 Doc. Version 9.01
  Desktop Suite End User pro added